| Tree No. | Species | Height (m) | Stem diam @1.5m (mm) | Crown spread (m) | Crown clearance(m) & direction of lowest growth | Maturity | Vigour | Est remaining contribution (yrs) | Condition/ Comments | Preliminary Management recommendations | Ultimate crown radius (m) | RPA radius (m) | BS5837 quality ref |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| T1 | Elm | 12 | 600# | N 5 S 6 E 5 W 5 | 2.5 4.0m E | Y | P | <10 | On adjacent private land, partly overhanging Library site. Extensive crown dieback due to Dutch Elm Disease. | Inform private owner of extensive dieback and advise tree is felled. | N/A | 7.2 | U |
| T2 | Purple Plum | 10 | 330 | N 4 S 4 E 4 W 3.5 | 3 | M | F | 10+ | Dense crown, number of structurally weak branches | None | 4 | 3.9 | C |
| G3 | Group containing Silver Birch x3 | 12 | 390 390 210 | N 4.5 S 5 E 4 W 4 | 1.5 3.0m E | Y/M | G | 20+ | Prominent group, generally well formed with some exudate on one stem. Power lines located to the east which touching some small branches and some low growth over the footpath. | Crown lift over the footpath to 3m by shortening branch tips and keeping cuts <50mm diameter. Advise power company about pruning small branches from power lines. | 7 | 4.8 | A |
| T4 | Cut-leaved Norway Maple | 4 | 170 | N 2.5 S 2 E 2.5 W 2 | 2.5 2.5 N | Y/M | G | 40+ | Unusual tree cultivar. Well formed tree. Some basal suckers will need removing in the future. | None | 5 | 2.1 | B |
| T5 | London Plane | 15 | 530 | N 6 S 6 E 7 W 5 | 1.5 | Y/M | G | 40+ | Feature tree, prominent street scene location | None | 10 | 6.3 | A |
| T6 | Lawsons Cypress | 6 | 450# | N 3 S 3 E 3 W 2 | 0.0 | M | G | 20+ | Well-formed conical tree at the front of the site. | None | 5 | 5.4 | C |
| T7 | Ash | 9 | 500# | N 5# S 5# E 5# W 6 | 2.0 | Y/M | G | 20+ | On adjacent private land, overhangs the site. The grass area adjacent to the boundary is likely to contain roots from this tree. | None | 8 | 6.0 | C |
| T8 | Ash | 13 | 600# | W 5 | >4 | OM | P | 10 | Private tree overhanging site. Declining vigour, has been crown thinned. Crown spread measured only from boundary hedge. | None | N/A | 7.2 | C |
| T9 | Goat Willow | 7 | 440 270 | N 3.5 S 4.5 E 3.5 W 5 | 1.2 | Y/M | G | 40+ | Twin stemmed tree from 1m, growing very close to a covered bin store. Probably self-set. | None | 6 | 5.2 | C |
| T10 | Indian Bean tree | 7 | 340 | N 3.5 S 4.5 E 3.5 W 5 | 0.6 | Y/M | G | 40+ | Reasonably well-formed tree, close to the existing building with branch tips touching. | None | 7 | 4.1 | B |
| T11 | Oak | 7 | 110 | N 2 S 2 E - W 2 | nil | Y | G | 40+ | Commemorative Shrops Star Millenium oak. Good tree for the future. C category because stem dia. under 150mm, otherwise would be B category | Crown lift if retaining | 10 | 1.3 | C |
| T12 | Oak | 16 | 950# | N 10# S 9 E 8 W 10 | 1.0 3.5m S | M | G | 40+ | Very large feature tree. In boundary hedge. Has been lightly reduced in the past and has a small basal cavity but not considered significant at present. | None | 10 | 11.4 | A |
| T13 | Red Horse Chestnut | 7 | 330 | N 4 S 4 E 3 W 3 | <1 | Y/M | G | 20+ | Minor bleeding canker infection. Extension growth & foliage good. | None | 8 | 3.9 | C |
| T14 | Red Horse Chestnut | 6 | 370 | N 4.5 S 5 E 3 W 4 | 1.8 | Y/M | P | <10 | Infected with bacterial bleeding canker, crown is thin and the tree is not likely to survive for long. | Remove when site use changes | 8 | 4.5 | U |
| T15 | Red Horse Chestnut | 6 | 450 | N 4 S 5 E 4.5 W 4 | 1.8 | Y/M | G | 40+ | Minor bacterial bleeding canker infection. | None | 8 | 5.4 | C |
| T16 | Horse Chestnut | 9 | 600 | N 5 S 5 E - W 6 | 1.5 | Y/M | G | 20+ | Heavy Leaf Minor infestation. Minor bleeding canker infection. Would be B category without infections | None | 10 | 7.2 | C |
| T17 | Horse Chestnut | 7 | 450 | N 3 S 3 E 3 W 3 | 2.0 | D | N | 0 | Dead tree that has lost a large limb. As site not currently being used ok to retain at present but will have to be removed when site usage alters. | Remove when site use changes | N/A | 5.4 | U |
| T18 | Horse Chestnut | 10 | 370 | N 4 S 4.5 E 3 W 5 | 1.0 | Y | F | <10 | Heavily infected with bacterial bleeding canker and leaf miner, unlikely to survive for long. | Remove when site use changes | 8 | 4.5 | U |
| T19 | Sycamore | 13 | 790 (measured @ 70cm agl) | N 4.5 S 7 E 4+ W 5 | 2 | M | G | 40+ | Divides in to 3 stems at 1.5m. Included compression unions. Branches on SE side overhang private garden & are nearly touching roof of property. | Reduce branches over private garden. | 10 | 9.6 | C |
| T20 | Oak | 16 | 900# | N 8# S 8# E 10# W 8# | 1.2 3.0m W | M | G | 40+ | Outside fenced site in amongst dense shrubby vegetation. Overhangs the site significantly. There has been selective branch reduction over site in the past. Likely to be a lot of roots growing on site side. Veteran tree | None | 10 | 15 | A |
| G21 | Group containing White Poplar x1, Oak x1 & Ash x1 | 17 | 600# (Pop) 300# AshOak | N 3# S 3# E 8# W 3# | 1.2 | Y/M | G | 40+ | White Poplar on private land but Oak & Ash located outside fenced site on far side of footpath, possibly inside site boundary All in good health but difficult to assess due to vegetation. Branches overhang the site and likely to be rooting into the site. | None | 8 | 3.6 | B |
| T22 | Oak | 18 | 800# | N 8# S 8# E 8# W 8# | 2.0 | M | G | 40+ | Not able to inspect as surrounded by dense vegetation. Crown is healthy. Tree is outside the fenced site and on the far side of the dry ditch. Possibly outside site boundary but likely there will be some rooting within the site. Veteran tree. | None | 10 | 15 | B |
| G23 | Ash x 5, Cherry x1, Spruce x 2 | 14 Aver | 150 - 500 | - | < 2 | Y/M | F - G | 20+ | Majority are poorly formed |  | 7 | 6.0 | C |
| T24 | Ash | 11 | 500# | N 4 S 5 E 5 W 5 | 1.5 | Y/M | F | 30+ | Dense ivy cover & location between 2 fences inhibited inspection |  | 8 | 6.0 | C |
| T25 | London Plane | 12 | 570 | NE 8 # E 7 W 8# | 1.0 3.0m W | Y/M | G | 40+ | On the edge of a former playground in an elevated location. Has slabs around the base and has palisade fencing on the far side. The ground level drops significantly very close to base of tree | None | 10 | 6.9 | B |
| T26 | Silver Weeping Lime | 13 | 500 | N 3.5 S 4 E 3 W 4 | nil | Y/M | G | 40+ | Excellent feature tree on road side frontage. | Remove tarmac around base to leave at least 1m clear radius | 8 | 6.0 | A |
| T27 | Oak | 7 | 300 | N 3# S 3 E 3 W 3 | 1.5 | Y | G | 40+ | Adjacent to boundary hedge, reasonably formed and well-established tree. | None | 10 | 3.6 | B |
| T28 | Oak | 16 | 700# | N 6# S 8# E 6# W 9# | 2.5 | M | G | 40+ | Outside fenced area but on the edge of a dry ditch. Canopy overhangs the site by 4m and roots are likely to be present within the site. Veteran tree | None | 10 | 15 | A |
| G29 | Oak x2 | 17 | 900# | N 8 | 2 | M | G | 40+ | One tree twin stemmed growing from old bole & one single stemmed tree. Both have veteran characteristics. Important trees.Total canopy length of trees from E – W 26m | None | N/A | 15 | A |
| T30 | Oak | 18 | 1400# | N 7 S 7# E 7 W 8 | 1.8 4.0 NW | L/M | G | 40+ | Has had large limbs (800mm diameter) removed over adjacent property in past couple of years. Tree borders adjacent fence of property. A veteran due to its very large girth. Broad crown | None | N/A | 15 | A |
| G31 | Group containing Field Maple x2 | 14 | 300 (200 x2) | N 5 S 3# E 5 W 6 | 1.5 4.0 NW | M | G | 20+ | Mature trees in old hedgeline. Drawn up examples but in good health. One tree twin stemmed. | None | N/A | 3.6 | B |
| T32 | Oak | 10 | 1000+# | N 5 S - E 4 W 4 | 3 | OM | P | 10+ | Dense hedge growth preventing clear view of stem. Veteran tree. Previous poor quality reduction & thinning work not helped ailing tree. Crown density <50% | None | N/A | 15 | B |
| T33 | Cherry | 7 | 400 | N 5 S 5.5 E 5 W 5 | 2.0 | M | G | 20+ | Healthy prominent tree. | None | 6 | 4.8 | B |
| T34 | Sycamore | 11 | 530 | N 6 S 6 E 5 W 5 | 2.0 | Y/M | G | 40+ | On adjacent land in grassed area. The rooting area will be biased towards the site owing to hard surfacing to the west. Canopy overhangs the site by 2m. | None | 10 | 6.3 | A |
| T35 | Sycamore | 8 | 300# | N 3 S 3 E 3 W 3 | 1.5 | Y | G | 40+ | Only viewed from outside dense scrub area. | None | 10 | 3.6 | C |
| T36 | Common Alder | 6 | 185 | N 2 S 2 E 2 W 2 | 1.5 | Y | G | 40+ | One in a group of 4 trees in front of church | None | 6 | 2.5 | C |
| T37 | Common Alder | 5 | 120 120 90 | N 2.5 S 1 E 1 W 2 | 1.20 | Y | F | 20 | Multi stemmed. Poor form. One in a group of 4 trees | None | 6 | 1.5 | C |
| T38 | Common Alder | 7 | 160 | N 3 S 1 E 1.5 W 2 | 1.5 | Y | G | 40 | One in a group of 4 trees. | None | 6 | 1.9 | C |
| T39 | Japanese Cherry | 5 | 240 @ 90cm | N 1 S 3 E 3 W 2 | 2 | Y/M | G | 30 | Poorly formed stem but low risk of failure. One in a group of 4 trees | None | 5 | 3.0 | C |
| T40 | Common Alder | 8 | 325 | N 3.5 S 3 E 3.5 W 3 | 1.8 | Y/M | G | 40+ | Near entrance path to building, well-formed tree, part of a group. Hard surfacing within 1.5m of the base on 2 sides. | None | 6 | 3.9 | A |
| T41 | Common Alder | 8 | 250 | N 1.5 S 1.5 E 1.5 W 2 | 1.5 | Y | G | 40+ | In shrub bed near entrance path to the building. | None | 6 | 3.0 | B |
| T42 | Common Alder | 8 | 200 | N 1.5 S 1.5 E 1.5 W 2 | 1.2 | Y | G | 40+ | On grassed area bordering road, part of a larger linear group. | None | 6 | 2.4 | B |
| G43 | Group containing Alder x5 | 8 | Av. 225 | N 2 S 2 E 2 W 2 | 1.8 | Y | G | 40+ | Linear group closely planted adjacent to the road and within 1m of the footpath. | None | 6 | 2.7 | B |
| G44 | Group of 30+ comprising Oak, Ash, Birch & Sycamore | 12 | 150 - 350 | 6 max on W side | 1.5 | Y/M | G | 40+ | Screening value. Some of outer edge trees well formed, inner trees suppressed & less well formed | None | 10 | 3.0 | B |
| T45 | Himalayan Birch | 7 | 200 @ 1.2m | N 2 S 2 E 3 W 2 | 1.8 | Y | G | 40+ | Average form as it becomes multi-stemmed at 1.2m. | None | 6 | 2.4 | C |
| G46 | Group containing Rowan x1, Swedish Whitebeam x1 & Snowy Mespilus x1 | 5 | Av. 110 | N 2 S 2 E 2 W 2 | 1.6 | Y | G | 40+ | Moderately formed trees in good health. | None | 5 | 1.2 | C |
| T47 | Himalayan Birch | 8 | 220 | N 3.5 S 2 E 3 W 3 | 1.0 | Y | G | 40+ | Well-formed tree with a sunken footpath 1m to the south in which little rooting would be expected. | None | 6 | 2.7 | B |
| T48 | Norway Maple | 7 | 210 | N 2 S 3 E 2.5 W 3 | 1.5 | Y | G | 20+ | A small tree that is poorly formed with weak branch unions developing. Possibly a reversion of a variegated cultivar. | None | 8 | 2.3 | C |
| G49 | Group of 25+ fruit trees, Crack Willow & Ash | 13 max | 200 Aver | - |  | Y/M | G | 40+ | Screening value. Fruit trees <5m height. Larger trees at back of group poor – moderate form. | None | N/A | 2.4 | C |
| G50 | Field Maple x 3 | 8 | 250# | - | 1 | Y/M | G | 40+ | In boundary hedge line, overhanging on N side (York House) by 2m | None | 6 | 3.0 | C |
| G51 | Group of multistemmed Crack Willow | 15 | 300 - 500 | - | 2 | Y/M | F | 20 | Situated o/s development site boundary but overhanging car park. Multi stemmed. Overhang of 5m measured from hedge. | None | 10 | 4.8 | C |

Key:

Maturity – This is a categorisation of the age class or life stage of a tree. There are 5 categories as follows:

Young (Y) – a tree less than one third of its normal life expectancy for the species and usually showing monopodial growth; Young/Mature (Y/M) – a tree between one and two thirds of its optimum life expectancy for the species normally showing sympodial growth form; Early-mature (E/M) – a tree between two thirds and its optimum life expectancy for the species but that has a naturally smaller crown size and shape for than would be expected for the species; Mature (M) – a tree between two thirds and its optimum life expectancy generally that has reached peak crown size and shape for the species; Late-mature (M) – in excess of its optimum life expectancy for the species usually with signs of crown decline. Veteran trees fall into this category and they offer numerous ecological habitats due to e.g. crown cavities, dead branches, loose bark etc and can have historic & cultural attributes.

Vigour – An assessment of the biological function of the tree by visually observing the leaf colour, size, crown density, general shoot extension and live crown. There are 4 categories as follows:

Good – attributes considered normal for species and variety; Fair -minor reductions within the tree crown of any of the categories listed from that of a normal example; Poor  - significant reductions within the tree crown of at least two categories listed accompanied by extensive crown dieback (in excess of 33% of crown volume); None - this is when a tree is dead

Est remaining contribution (yrs) - This is an estimation of how long the particular trees is likely to survive in a similar form, size, shape etc in the current location, measured in years. Issues such as reduced vigour, pathogen infection or a likelihood of structural failure are major factors reducing this value (categories are 40+, 20-40, 10-20, <10).

RPA radius (m) – This is the radius, in metres, of the root protection area (RPA) being expressed as a circle around each tree.

RPA area (m2) – This is the equivalent cross-sectional area of the root protection area (in square metres) which is deemed large enough to contain sufficient volume of roots to maintain the tree’s viability.

BS5837 quality ref: This is a grading based on Table 1 within the standard and has 4 categories and 3 subcategories. The 4 main categories are:

A - trees of high quality with an estimated remaining life expectancy of at least 40 years.

B - trees of moderate quality with an estimated remaining life expectancy of at least 20 years.

C - trees of low quality with an estimated remaining life expectancy of at least 10 years, or young trees with a stem diameter below 150mm.

U - those in such a condition that they cannot realistically be retained as living trees in the context of the current land use for longer than 10 years